Silk 700S. Bearings used on the bike

Crankshaft.

RNA 4906 Bearing inner 2off

INA 30x35x18 or 20 Inner race 2off

RNA 4905 Bearing outer 2off

RHP 6005 Location bearing 1 off

B407 and B 524 Crank end oil seals 1 off each

SE 46 Caro bronze Small end bush

Durkopp 25x32x16 Big end bearing (silver plated) 2off (ask me,) )Clive Worrall)

Oil pump.

Glacier 06 Du 06 Spindle bush 1off  7/16od x 3/8id

Spindle oil seal 1off (mod) 3/4od x 3/8id x 1/4w

Cover bush iolite 3/8od x 1/4id

Clutch release.

INA K 81109 radial roller bearing 1off

INA 4565 Thrust washer 1off

TTO E558 4 SC 218 168 18  Lifting plate seal 1off   Odd imperial size difficult to find, 2-3/16od x 1-11/16id x 3/16w

Clutch.

INA K90x97x20 Clutch centre bearing 1off

Kick start.

RHP 6004 2RS Kickstart housing bearing 1off 40od x 20id x 14w

Caro bronze se46 Layshaft /kickstart shaft bush 1off (early bikes or safer option)

INA15x19x13                   As above                    1off (later bikes, better performance but requires changing periodically)

Gearbox and Final drive.

20x32x7 oil seal Final drive seal plate 1off

RHP6206 2RS Final drive casting bearing 1off (engine sprocket out rigger)

Fafnir XM35 sleeve gear bearing 1off RHP6007 62x35x14

RHO6301 End cover main shaft bearing 1off 37x12x12

SWB 2608 Sleeve gear bushes 2off

Other gears made to suite.

RHP LS7A2 Gearbox layshaft bearing 1off  1-9/16od x 5/8id x7/16w

Foot control lever bush MB 1525 DX 2off  17x15x25

Front and rear wheel bearings RHP 6303 2RS

Cush drive bearing RHP6205 2RS 1 off

Steering head bearing Taper roller  2 inch od x inch id 2off

Fork seals 38x50x7 2off per leg